LED 18 x 6in1 waterproof par

- schematics section：

A．The function keys

B．Add key

C．The reduction of key

D．Enter key

E．LED screen

A       B      C     D

The LED display window function, (all function according to the selected and then press the D key to confirm)

| Channel | display | Functional specifications |
| --- | --- | --- |
| 1 | A001 | Ten channel address code, (001-512), B, C key to add and subtract address code values |
| 1 | D001 | Six channel address code, (001-512), B, C key to add and subtract address code values |
| 2 | CC 00 | 7 colour jump to change, (01-99) B, C key to modify jump speed |
| 3 | EE 00 | Colorful gradient (01-99) B and C modify pulse variable, velocity gradient |
| 4 | FF 00 | 7 colour pulse variable, (01-99) B, C key to modify combination change speed |
| 5 | BEBF | 7 colour acoustic change |
| 6 | R220 | Red colors, (000-255), B and C key change colors |
| 7 | G220 | The green colors, (000-255), B and C key change colors |
| 9 | B220 | Blue colors, (000-255), B and C key change colors |
| 10 | W220 | White colors, (000-255), B and C key change colors |
| 11 | Y220 | Yellow colors, (000-255), B and C key change colors |
| 12 | P220 | Purple colors, (000-255), B and C key change colors |

3．DMX512  10CH

| Channel | function | instructions |
| --- | --- | --- |
| 1 | Tuned light | R、G、B、W、Y、P Tuned light, linear light, from dark to bright |
| 2 | Total stroboscopic | R、G、B、W、Y、P Total stroboscopic, from slow to fast |
| 3 | Feature selection | 0-50: DMX 9 channel control;51-100: jump;101-150: the gradient;151-200: pulse variable;201-255: voice control |
| 4 | Function of speed | Function of speed, from slow to fast |
| 5 | R | R dimming , linear dimming, from dark to bright |
| 6 | G | G dimming , linear dimming, from dark to bright |
| 7 | B | B dimming , linear dimming, from dark to bright |
| 8 | W | W dimming , linear dimming, from dark to bright |
| 9 | Y | Y dimming , linear dimming, from dark to bright |
| 10 | P | P dimming , linear dimming, from dark to bright |

4．DMX512  6CH

| Channel | Function | Specification |
| --- | --- | --- |
| 1 | R | R dimming , linear dimming, from dark to bright |
| 2 | G | G dimming , linear dimming, from dark to bright |
| 3 | B | B dimming , linear dimming, from dark to bright |
| 4 | W | W dimming , linear dimming, from dark to bright |
| 5 | Y | Y dimming , linear dimming, from dark to bright |
| 6 | P | P dimming , linear dimming, from dark to bright |