Please read the instructions carefully before use

350W beam lamp shaking head lamp

Use an explanatory book

(Color display)

Orders to record

Chapter 1 Precautions and Installation	1

1.	maintenance	1

2.	The statement	1

3.	Product Precautions	1

4.	Product introduction	1

5.	Signal Line connection (DMX)	2

6.	Installation of lamps and lanterns	2

Chapter 2 Panel operation	3

1.	The key that	3

2.	operation	4

1.	Manual control	4

2.	Set up the	5

3.	System information	6

Chapter 3 Channel description	7

1.	The channel table	7

Chapter 4 common faults and attention to use	10

1.	Troubleshooting Common Faults	11

2.	Precautions for Use	11

Precautions and Installation

maintenance

- The lamp should be kept dry, avoid working in damp environment.

- Intermittent use will effectively prolong the life of the lamps.

- For good ventilation and lighting, take care to clean fans and fan nets and lenses frequently.

- Do not use alcohol and other organic solvents to wipe the lamp shell, so as not to cause damage.

The statement

When this product leaves the factory, the performance is intact, the package is complete.All users shall strictly abide by the warning and operation instructions stated above. Any damage caused by misuse is not guaranteed by the Company, and the distributor shall not be responsible for the faults and problems caused by ignoring the operation manual.

This manual is subject to technical changes without prior notice.

Product Precautions

- In order to ensure the service life of the product, do not put it in the damp or leaking place, and do not work in the environment where the temperature exceeds 60 degrees

- Do not place the product in places where it is easy to loose or shake.

- In order to avoid the danger of electric shock, please seek professional help for the maintenance of this product.

- When the bulb is used, the voltage change of the power supply should not exceed ±10%. If the voltage is too high, the life of the bulb will be shortened. If the voltage is too low, the light color of the bulb will be affected.

- After power off, it is necessary to use the lamp to cool down fully after 20 minutes before power on again.

- To ensure the normal use of this product, please read this instruction carefully.

Product introduction

- Light source power: 380W Phoenix Light Bulb;

- Power supply: high efficiency and reliable switching power supply;

- Color plate: one color plate, each color plate is composed of 13 color plates + white light;

- Pattern plate: 14 pattern effects;

- Large adjustable range of beam Angle;

- Lens group optical system, electric focus, beam Angle 3.8°-45° linear adjustable;

- Horizontal 540°, 8Bit/16Bit resolution;

- Vertical 270°, 8Bit/16Bit resolution;

- Overheating protection;

- Control mode: DMX512/ master slave/automatic;

- Protection class: IP20;

Signal Line connection (DMX)

Use rs-485 cables that meet specifications: shielded, 120ohm characteristic impedance, 22-24 AWG, low volumetric reactance.Do not use microphone cables or cables with different specified characteristics.Terminals must be connected using 3 - or 5-pin XLR male/female connectors.An impedance matching resistor of 120ohm (minimum 1/4 W) must be inserted between terminals 2 and 3 of the terminal plug.

Important: Wires should not touch each other or metal enclosures.

Figure 1 Schematic diagram of DMX signal cable connection

Installation of lamps and lanterns

Lamps can be placed horizontally, diagonally or upside down.Be sure to pay attention to the installation method when slant and upside down.

As shown in Figure 2, it is necessary to ensure the stability of the installation site before positioning the lamp. During the installation of the inverted hanging, it is necessary to ensure that the lamp does not fall off from the support frame, and the safety rope should be used to pass through the support frame and the handle of the lamp for auxiliary hanging to ensure safety. Prevent lamp from falling and sliding.

During the installation and debugging of the lamps, pedestrians are not allowed to pass under the lamps. Check regularly whether the safety ropes are worn or the hook screws are loose.

Our company will not assume any responsibility for any consequences caused by falling of the lamp due to unstable hanging installation.

FIG. 2 Schematic diagram of upside-down lamps

Panel operation

- The key that

FIG. 3 Schematic diagram of panel keys

The following takes "modify DMX address code" as an example to describe the use of keys:

1. If the current screen is not the main screen, press the "Left" key (one or more times) to return to the main screen

2. On the home screen, press the Up or Down key to select the Settings button

3. Press "OK" to enter the "Settings" interface

4. In the "Settings" interface, press "Up" or "Down" to select "DMX Address".

5. Press "OK" to enter editing mode

6. Press the "Up" or "Down" key to modify DMX address code

7. Press OK to exit the editing mode

- operation

FIG. 4 Schematic diagram of main menu description

manual

This interface is used to control the current lamps and lanterns, and automatically enter the host state (do not receive DMX signal, send DMX signal to the bus to the slave).

The manual menu will display 16 channels or 20 channels according to the standard 16 channel or extended 20 channel mode set in the Settings menu.

| options | instructions |
| --- | --- |
| 1CH. X | 0 ~ 255 | Press "OK" to enter editing mode.At this time, select the hundreds and press the "up" and "down" keys to change the channel value.Press OK again to select the ten place edit.Press "OK" again to select the bits to edit.Press again to exit the edit mode |
| ... | 0 ~ 255 |  |
| 15 ch. Focus | 0 ~ 255 |  |
| 16 ch. Reset |  | Press "OK" to see the confirmation dialog box. Press "OK" again to enter the reset interface and reset all the motors |
| 16CH. Bulb control | open |  |
|  | guan |  |
| 17 ch. Keep | 0 ~ 255 | This parameter is displayed when the channel mode is Extended CH20 |
| 18CH. Color wheel speed | 0 ~ 255 | This parameter is displayed when the channel mode is Extended CH20 |
| 19CH. Dimming - Prism - atomization speed | 0 ~ 255 | This parameter is displayed when the channel mode is Extended CH20 |
| 20CH. Pattern disc speed | 0 ~ 255 | This parameter is displayed when the channel mode is Extended CH20 |

Set up the

| options | instructions |
| --- | --- |
| The operation mode | DMX | Slave state: receiving DMX signal from console or host |
|  | Since the walk 1 | Host state: self-powered and sends DMX signal to slave |
|  | Since 2 |  |
|  | random |  |
|  | Voice control |  |
| DMX address | 1-512 | Press "OK" to enter editing mode.At this time, select hundreds and press the "up" and "Down" keys to change the address code.Press OK again to select the ten place edit.Press "OK" again to select the bits to edit.Press again to exit the edit mode |
| The channel model | Standard 16 ch | Standard 16-channel mode, channels 17 to 20 are invalid |
|  | Extended 20 ch | Extended 20 channel mode, 17th to 20th channel control speed (see channel table) |
| X inversion | guan |  |
|  | open |  |
| Y inversion | guan |  |
|  | open |  |
| XY exchange | guan |  |
|  | open | Channels for exchanging XY axis (including fine tuning) |
| XY encoder | open | Use an encoder (optocoupler) to determine out-of-step and automatically correct position |
|  | guan | No encoder (optocoupler) is used to correct position |
| DMX signal | keep | Continue running as before |
|  | remove | Motor back, stop running |
| Switch on light bubble | guan | Directly reset after power on, no light bulb (need to use menu or console to manually light bubbles) |
|  | open | After the bulb is powered on, it will automatically light up and reset until the bulb successfully lights up |
| Color wheel changes linearly | open | Color wheel changes linearly |
|  | guan | Color wheel nonlinear change, half-color change |
| Restore default Settings |  | Press OK to see the confirmation dialog box. Press OK again to restore the default Settings |

system

| options | instructions |
| --- | --- |
| DIS |  | Display board software version |
| MT |  | Motor board software version |
| Reset the calibration | The X axis calibration | After entering the sub-interface, you can adjust the reset position of the X axis, Y axis and other motors to compensate for errors in hardware installation. The adjustment range is -128~+127, +0 means no adjustment. |
|  | The Y axis calibration |  |
|  | Color calibration |  |
|  | Design of the calibration |  |
|  | Focusing calibration |  |
|  | The dimming calibration |  |
|  | Prism 1 calibration |  |
|  | Prism 2 calibration |  |
|  | Atomization calibration |  |
| Sensor monitoring | The X axis hole, | 0 when magnetic is detected, 1 otherwise |
|  | Y hall | 0 when magnetic is detected, 1 otherwise |
|  | Color wheel hall | 0 when magnetic is detected, 1 otherwise |
|  | Pattern disc hall | 0 when magnetic is detected, 1 otherwise |
|  | Adjustable JiaoHuoEr | 0 when magnetic is detected, 1 otherwise |
|  | Prism 1 Hall | 0 when magnetic is detected, 1 otherwise |
|  | Prism 2 Hall | 0 when magnetic is detected, 1 otherwise |
|  | X-axis encodes disk status | Two digits, each corresponding to a photoelectric switch on the coding disk |
|  | Y-axis encodes disk status | Two digits, each corresponding to a photoelectric switch on the coding disk |
|  | X-axis encoding disk step value | In the positive direction, the step value should increase, in the opposite direction, the step value should decrease.The same value is normal every time you turn to the same point |
|  | Y-axis encoding disk step value | In the positive direction, the step value should increase, in the opposite direction, the step value should decrease.The same value is normal every time you turn to the same point |
| System error |  | If the red ERR indicator lights up, it indicates that the lamp is running wrong. Details can be viewed in the sub-interface.After viewing, you can press the "Clear" button to clear error records |
| DMX monitoring |  | Real-time monitoring console signal |

| The error message | instructions |
| --- | --- |
| MT board connection failed. Procedure | Motor board is not responding.The serial communication line connecting the display board to the motor board is faulty, or the motor board is faulty. |
| The X-axis reset fails | X-axis photoelectric switch, or X-axis motor or motor board problem |
| The Y-axis reset fails | Y photoelectric switch, or Y motor or motor board problem |
| X-axis Hall error | X axis Hall, or motor plate problem |
| Y-axis Hall error | Y axis Hall, or motor plate problem |
| The color disk failed to reset. Procedure | Color plate Hall, or color plate motor problem |
| Failed to reset the pattern disk | Pattern plate Hall, or pattern plate motor problem |
| The focus reset failed | There is a problem with the focusing hall or the focusing motor |
| Bulb control failure | Failed to light or extinguish the bubble. The light lighter or bulb is faulty |

The channel description

  - The channel table

| channel | The channel model |
| --- | --- |
|  | 16 | 20 |
| 1 | X | X |
| 2 | Y | Y |
| 3 | X fine-tuning | X fine-tuning |
| 4 | Y fine-tuning | Y fine-tuning |
| 5 | XY speed | XY speed |
| 6 | Atomization & colorful | Atomization & colorful |
| 7 | Light cutting/stroboscopic | Light cutting/stroboscopic |
| 8 | The dimmer | The dimmer |
| 9 | The color wheel | The color wheel |
| 10 | Pattern plate | Pattern plate |
| 11 | Prism 1 | Prism 1 |
| 12 | Prism 1 rotation | Prism 1 rotation |
| 13 | Prism 2 | Prism 2 |
| 14 | Prism 2 rotation | Prism 2 rotation |
| 15 | focusing | focusing |
| 16 | Bulb & Reset | Bulb & Reset |
| 17 |  | There is no |
| 18 |  | Color wheel speed |
| 19 |  | Dimming - Prism - atomization speed |
| 20 |  | Pattern disc speed |

Channel parameter values (full version) :

| channel | function | Channel numerical | The effect |
| --- | --- | --- | --- |
| 1 | The X axis | 000-255. | Horizontal scan 540 degrees |
| 2 | Y | 000-255. | Vertical 270 degree scan |
| 3 | The X axis fine-tuning | 000-255. | Level 1.2 degrees fine tuning |
| 4 | Y fine-tuning | 000-255. | 1.2 degrees vertical fine tuning |
| 5 | XY speed | 000-255. | The speed goes from fast to slow |
| 6 | Atomization & colorful | 000-127. 128-191. 192-255. | There is no Atomizing blade cut Multicolored cut |
| 7 | stroboscopic | 000-003. 004-103. 104-107. 108-207. 208-212. 213-251. 252-255. | Brake light off Stroboscopic from slow to fast Light switch open → (controlled by dimming channel) Pulse stroboscope from slow to fast Light switch open → (controlled by dimming channel) Random stroboscopic from slow to fast Light switch open → (controlled by dimming channel) |
| 8 | The dimmer | 000-255. | From dark to bright |
| 9 | Color plate | 000-004. 005-009. 010-014. 015-019. 020-024. 025-029. 030-034. 035-039. 040-044. 045-049. 050-054. 055-059. 060-064. 065-069. 070-074. 075-079. 080-084. 085-089. 090-094. 095-099. 100-104. 105-109. 110-114. 115-119. 120-124. 125-129. 130-134. 135-139. 140-144. 145-149. 140-200. 201-255. | The white light White light + color 1 Color 1 Color 1 plus color 2 2 colors Color 2 plus color 3 The color of 3 Color 3 plus color 4 4 color Color 4 plus color 5 Color 5 Color 5 plus color 6 Color 6 Color 6 plus color 7 Seven colors Color 7 plus color 8 Color 8 Color 8 plus color 9 Color 9 Color 9 plus color 10 Color 10 Color 10 plus color 11 Color 11 Color 11 plus color 12 Color 12 Color 12 plus color 13 The color of 13 Color 13 plus color 14 The color of 14 Color 14+ white light Forward flow (from fast to slow) Reverse flow (from slow to fast) |
| 10 | Pattern plate | 000-004. 005-009. 010-014. 015-019. 020-024. 025-029. 030-034. 035-039. 040-044. 045-049. 050-054. 055-059. 060-064. 065-069. 070-125. 126-130. 131-190. 191-195. 196-200. 201-205. 206-210. 211-215. 216-220. 221-225. 226-230. 231-235. 236-240. 241-245. 246-250. 251-255. | In figure 1 In figure 2 In figure 3 In figure 4 In figure 5 In figure 6 In figure 7 In figure 8 In figure 9 Solid figure 10. In figure 11. In figure 12 In figure 13 In figure 14 Forward flow (from fast to slow) stop Reverse flow (from slow to fast) Solid figure 2 Jitter (from slow to fast) Solid figure 3 Jitter (from slow to fast) Solid Figure 4 Jitter (from slow to fast) Figure 5 Jitter (from slow to fast) Figure 6 Jitter (from slow to fast) Figure 7 Jitter (from slow to fast) Figure 8 Jitter (from slow to fast) Solid figure 9 Jitter (from slow to fast) Solid figure 10 Jitter (from slow to fast) Solid figure 11 Jitter (from slow to fast) Solid figure 12 Jitter (from slow to fast) Figure 13 Jitter (from slow to fast) Figure 14 Jitter (from slow to fast) |
| 11 | Prism 1 | 000-127. 128-255. | Prism 1 pops up Prism 1 cut in |
| 12 | Prism 1 rotation | 000-127. 128-187. 188-195. 196-255. | Prism Angle adjustment Reverse rotation (from fast to slow) stop Forward rotation (from slow to fast) |
| 13 | Prism 2 | 000-127. 128-255. | Prism 2 pops up Prism 2 cutting |
| 14 | Prism 2 rotation | 000-127. 128-187. 188-195. 196-255. | Prism Angle adjustment Reverse rotation (from fast to slow) stop Forward rotation (from slow to fast) |
| 15 | focusing | 000-255. | Design clarity from far to near |
| 16 | The light bulb control | 000-099. 100-105. 200-205. 250-255. | Invalid region Put out the light bulb Light bulb Reset of all motor |
| Expand the channels | 17 | keep | 000-255. | The speed goes from fast to slow |
|  | 18 | Color wheel speed |  |  |
|  | 19 | Dimming - Prism - atomization speed |  |  |
|  | 20 | Pattern disc speed |  |  |

Common faults and precautions for use

Troubleshooting Common Faults

Lamps and lanterns contain microcomputer circuit board, high voltage power supply and other professional parts, for your safety and product life, non-professionals do not remove lamps and lanterns and related accessories without authorization.

The light bulb not bright

Possible cause: The bulb is not completely cooled, or the bulb reaches its life, the treatment is as follows:

- Because of abnormal operation, the bulb is not completely cooled, should be allowed to cool the lamp body for more than 10 minutes, so that its internal completely restored to the normal state, and then start the power supply again;

- Check whether the bulb has reached its service life and replace it with a new one.

- Check whether the bulb and lamp lighter circuit leakage, off or poor contact;

- Replace a new light lighter.

The beams of light appear dim

Possible cause: The bulb takes a long time to use or the optical path is not clean. Handle it as follows:

- Check whether the bulb has reached its service life and replace it with a new one.

- Check whether optical components or bulbs are clean, and whether dust accumulates on optical components such as bulbs. Clean and maintain the bulbs and components in the lamps regularly.

Pattern projection blur

- Check that the electronic focus channel value is appropriate for the current projection distance.

Lamps work intermittently

Yes Cause: The internal line is in the protected state.

- Check whether the fan is running normally or dirty, causing the internal temperature of the lamps and lanterns to rise;

- Check whether the internal temperature control switch is closed;

- Check if the bulb has reached its useful life and replace it with a new one.

The lamp does not accept the control of the console after normal reset

Possible cause: The signal cable is faulty or the lamp parameter Settings are abnormal. Handle the fault as follows:

- 41. Check the starting address code and the connection of the DMX signal line (intact and loose).

- Add signal amplifier, add 120 ohm terminal resistance;

Luminaire does not start

Possible cause: The power supply line is bad, and the treatment is as follows:

- Check whether the insurance on the power input socket is fused, and replace the insurance;

- The vibration of lamps in long-distance transportation leads to poor line contact

- Check the input power supply, computer board and other connectors.

Precautions for Use

- Check whether the local power supply meets the rated voltage requirements of the product, and the leakage protector and overcurrent protector meet the load requirements.

- Do not use the power cable whose insulation layer is damaged. Do not lap the power cable to other wires.

- The lamps and lanterns use strong wind refrigeration, easy to dust, must be cleaned once a month, especially the cooling vent, otherwise it will be blocked by dust, resulting in poor heat dissipation, so that the lamps and lanterns appear abnormal.

- When installing the lamps and lanterns, the fixing screws must be fastened, and the safety cable should be added, and the regular inspection;

- When installing and positioning the lamps, the minimum distance between any point on the surface of the lamps and any combustible and explosive objects should be 10m, and the distance from the irradiation object should be 2.5m. Please do not install the lamps directly on the surface of combustible materials.

- The continuous working time of lamps should not exceed 10 hours, and the interval time of continuous starting lamps should not be less than 10 minutes, otherwise it will not be triggered normally because of the bulb overheating protection;

- The closing time of the switch valve should not exceed 5 minutes. If the light needs to be closed for a long time, the control console (lamp gun control channel) should be used to close the lamp gun.

- In order to ensure that multiple lamps can better comply with the scene effect, lamps should not be in the unfinished scene, that is, to start the next scene action, preferably this state should not exceed 3 minutes, to ensure that multiple lamps can operate synchronously.

- In the process of use, if the lamp is abnormal, stop using the lamp in time to prevent other faults;