Instructions for using the LED lights

40x4in1 LED city color

1. Chinese color screen display window function control table.

| primary menu | second-level menu | Level 3 menu | Level 4 menu | Level 5 menu | Windows default |
| --- | --- | --- | --- | --- | --- |
| hand movement | move | hand movement /DMX |  |  | DMX |
|  | static state | -》 | R | 000-255 | 255 |
|  |  |  | G | 000-255 | 255 |
|  |  |  | B | 000-255 | 255 |
|  |  |  | W | 000-255 | 255 |
|  | assemble | 000-255 |  |  | 200 |
|  | gradual change | 000-255 |  |  | 200 |
|  | sound control | 0-1 |  |  | 0 |
| set up | running mode | hand movement /DMX |  |  | DMX |
|  | DMX address | 001-512 |  |  | 001 |
|  | channel pattern | 4-8 |  |  | 8 |
|  | signal condition | Keep / clear |  |  | keep |
|  | Fan mode | Regular turn / control |  |  | controlled |
|  | The dimming number | 16 Bit / 8 Bit |  |  | 16 The |
|  | Refresh the frequency | 1-22K |  |  | 14K |
|  | The dimming curve | Linear / square / antisquare / S line |  |  | linear |
|  | degree-day | ℉/℃ |  |  | ℃ |
|  | Restore factory | Give up / determine |  |  | give up |
| system | V1.0 |  |  |  |  |
|  | centre /EN | centre /EN |  |  | centre |
|  | Pour show | Turn off / turn on |  |  | close |
|  | screensaver | Turn off / turn on |  |  | close |

2. English color screen display window function control table.

| primary menu | second-level menu | Level 3 menu | Level 4 menu | Level 5 menu | Windows default |
| --- | --- | --- | --- | --- | --- |
| Manual | Function | Manual/DMX |  |  | DMX |
|  | Static | -》 | R | 000-255 | 255 |
|  |  |  | G | 000-255 | 255 |
|  |  |  | B | 000-255 | 255 |
|  |  |  | W | 000-255 | 255 |
|  | Jump | 000-255 |  |  | 200 |
|  | Gradient | 000-255 |  |  | 200 |
|  | sound | 0-1 |  |  | 0 |
| Set_up | Function | Manual/DMX |  |  | DMX |
|  | DMX address | 001-512 |  |  | 001 |
|  | CH mode | 4-8 |  |  | 8 |
|  | DMXsignal | Maintain/Clear |  |  | Maintain |
|  | Fan mode | Control/Always |  |  | Control |
|  | Dimming bit | 16bt/08bt |  |  | 16 The |
|  | Frequency | 1-22K |  |  | 14K |
|  | Curve | Linear/Square/Anti/S-line |  |  | Linear |
|  | Thermometer | ℉/℃ |  |  | ℃ |
|  | reset | No /Yes |  |  | No |
| System | V1.0 |  |  |  |  |
|  | centre /EN | centre /EN |  |  | centre |
|  | lnverted | Off/On |  |  | Off |
|  | Screensaver | Off/On |  |  | Off |

- 3.LED background display window function control table, (in DMX Mode state, often press A key for 3-4 seconds to enter the D key to exit)

| order number | English | the Chinese language | function declaration |
| --- | --- | --- | --- |
| 1 | Administrator 235 Red current | Administrator mode 235 Red current | Red current, (020-255) default (235) |
| 2 | Administrator 235 green current | Administrator mode 235 Green current | Green current, (020- -255) default value (235) |
| 3 | Administrator 235 blue current | Administrator mode 235 Blue current | Blue current, (020-255) default (235) |
| 4 | Administrator 235 white current | Administrator mode 235 White current | White current, (020-255) default (235) |
| 5 | Administrator 235 Power limit | Administrator mode 255 power limitation | Total power limit, (050-255) default (255 no limit) |
| 6 | Administrator 001 Dimming speed | Administrator mode 001 The dimming speed | Dimming speed default (001) |
| 7 | Administrator 055 temperature | Administrator mode 055 Temperature setting | Light body temperature value setting, (40-80) default value (55) Note: the lamp body should be connected to the temperature control resistance before this function works |
| 8 | Administrator Off/1/2 LOGO | Administrator mode Close / 1 / 2 LOGO | LOGO |
| 9 | Administrator Turn on shut down Push》》》》 | Administrator mode open close propelling movement 》》》 | Push (host background push function) shut down does not push the default value to the slave (shut down) |
|  |  |  | Turn on The host pushes to the slave to update the slave (background) parameters and (advanced settings) parameters Note: The signal line between the host and the slave is connected and powered up, and the slave is set to DMX512 mode. After the host enters this option, the host should not rush to exit and wait for the success of the slave update. At this time, the host should press the confirmation key to exit. |

4.DMX512 8 channel description

| order number | function | explain |
| --- | --- | --- |
| Channel 1 | Total dimming | Total dimming, linear dimming, from dark to bright |
| Channel 2 | Total frequency flash | Total frequency strobe, from slow to fast |
| Channel 3 | FS | Where 0-5 is empty; 6-100 jump The 101-150 gradients 151-200 pulse changes 201-255 Voice control |
| Channel 4 | Functional speed | Functional speed, from slow to fast |
| Channel 5 | R aiming | R dimming, linear dimming, from dark to bright |
| Channel 6 | G aiming | G dimming, linear dimming, from dark to bright |
| Channel 7 | B aiming | B dimming, linear dimming, from dark to bright |
| Channel 8 | W aiming | W dimming, linear dimming, from dark to bright |

5.DMX512 4 channel description

| order number | function | explain |
| --- | --- | --- |
| Channel 1 | R aiming | R dimming, linear dimming, from dark to bright |
| Channel 2 | G aiming | G dimming, linear dimming, from dark to bright |
| Channel 3 | B aiming | B dimming, linear dimming, from dark to bright |
| Channel 4 | W aiming | W dimming, linear dimming, from dark to bright |